## Slide 1: Обновленная библиотека генераторов псевдослучайных чисел RNGAVXLIB
Мария Гуськова, МИЭМ НИУ ВШЭ, НЦЧ РАН
Л.Ю.Бараш, ИТФ им. Л.Д.Ландау
Л.Н.ЩУР, НЦЧ РАН
Научный фонд НИУ ВШЭ грант 18-05-0024 и программа “5-100”
Notes: Hello
As you maybe have read my name from the schedule, I am Mariia Guskova. A master student from Moscow institute of electronics and mathematics.
And today I will talk about random number generators and technology AVX512
In the next few slides I will explain what is avx512

## Slide 2: Введение
МИЭМ НИУ ВШЭ, 2018
Требования :
Хорошие статистические свойства
Большой период
Эффективность
Теория
Воспроизводимость
Функции пропуска кусков
Notes: I’m sure that all of you have used random numbers. Now there are a lot of random numbers generators
For computer simulation they should have next properties : statistical properties (random numbers should be uniformly distributed, correlations between independent parts of sequence shouldn’t exist), long period, generator should be fast and not to use a lot of resources such as memory
Some theorems about period and statistical properties should exist
Generator should produce the same sequence for all machines, operating system shouldn’t matter
And functions which allow to skip part of the sequence is necessary for generation in parallel threads

## Slide 3: Введение
МИЭМ НИУ ВШЭ, 2018
Генератор | Период | Размерность равно-распределения | Теория
MT19937 |  |  | 
MRG32K3A |  |  | 
LFSR113 |  |  | 
PHILOX4X32_10 |  |  | 
GM55 |  |  | 
Требования :
Хорошие статистические свойства
Большой период
Эффективность
Теория
Воспроизводимость
Функции пропуска кусков
Notes: In the table some generators and their properties are listed. Mersenne twister the first generator has the biggest period and dimension of equidistribution. That means vectors of 623 random numbers are uniformly distributed in the cube with 623 dimensions
Mrg Multiple Recursive Generator combined of linear generators and this gives him statistic properties better than linear generator has
Lfsr is based on shift register and is very fast
Philox is a counter based generator . It s passed statistical tests but has no theory about it, so there can be some pitfalls
Gm55 is a generator based on cat’s transformation
Has a long period

## Slide 4: SIMD (Single Instruction Multiple Data)
МИЭМ НИУ ВШЭ, 2018
SSE – 16 128-битных регистров + инструкции
AVX – 16 256- битных регистров + инструкции (числа с плавающей точкой)
AVX2- 16 256- битных регистров + инструкции (целые числа)
AVX512 – 32 512- битных регистров + инструкции
Notes: My purpose was to speed up generator using vectorization
There is a technology called SIMD and few extensions which implement it
Every extension consist of registers and instruction
sse allows to process 4 numbers simultaneously with the use of special commands
Avx can manage 8 number with floating point
Avx2 contains commands for processing integer data and some new commands
And the most recent avx 512 can process 16 numbers

## Slide 5: AVX512 Advanced Vector Extensions
МИЭМ НИУ ВШЭ, 2018
CDI
ERI & PHI
AVX-512F
AVX2
AVX
SSE
CDI
AVX-512F
AVX-512
VL, BW, DQ
AVX2
AVX
SSE
KNL Xeon Phi
Skylake Xeon
F (Foundation)
CDI (Conflict Detection Instructions)
ERI (Exponential and Reciprocal Instructions)
PFI (Prefetch Instructions)
BW (Byte and Word Instructions)
DQ (Doubleword and Quadword Instructions)
VL (Vector Length Extensions)
Notes: Avx 512 in turn is divided into several parts
The most general is AVX512F (foundation) it extends avx instructions to 512 mode
Now avx512 is only in intel architectures knl xeon phi and Skylake xeon
They are a little bit different in assembly

## Slide 6: Особенности AVX-512
МИЭМ НИУ ВШЭ, 2018
32 векторных регистра, каждый по 512 бит + 8 масочных регистров
Инструкции использующие масочные регистры
512-битные операции на упакованных числах с плавающей точкой или на целыми числами
Встроенный broadcast
Поддержка команд gather/scatter
Использование AVX и Intel AVX-512 инструкции без штрафов
Notes: On this slide some features of avx512 are listed
The registers of length 512 bit are called zmm , 255 are ymm
You can see that bigger registers contains the smaller
With avx512 extension commands you can work with ymm and xmm
Also there are 8 mask register .they have 16 bit length
For example
You can compare numbers in register with some constant a , the result will be placed into mask register
And then execute a command which will add some constant b for all numbers that are less than a
Embedded broadcasting allows a single value to be broadcast across a source operand, without requiring an extra instruction

## Slide 7: Библиотеки генераторов псевдослучайных чисел
МИЭМ НИУ ВШЭ, 2018
Библиотека | Генераторы | Реализации | Параллельные потоки
GNU Scientific Library | GFSR4, TAUS, TAUS2, RANLXS0, RANLXS1, RANLXS2, MT19937, MRG | ANSI C | 
Intel MKL Library | GFSR, MRG32k3a, MT19937 , MT2203, SFMT19937 , PHILOX4X32X10, ARS5 | SSE2, SSE3, SSSE3 | 
RNGSSELIB | MT19937, MRG32K3A, LFSR113, GM19, GM31, GM61 | ANSI C, SSE2 | 
SPRNG | PMLCG, LFG, MLFG, CMRG, PMLCG | C++ | 
TRNG | MRG_, MRG_S, YARN_, YARN_S, LAGFIB_XOR, LAGFIB_PLUS, MT19937 | ANSI C, CUDA | 
RNGAVXLIB | GM19, GM31, GM61, GM29, GM55, GQ58.1, GQ58.3, GQ58.4 , MT19937, MRG32K3A, LFSR113 | ANSI C, SSE2, SSE4.1, AVX2 | 
Notes: In this table you can see current libraries of random number generators
The first one gnu scientific library include lots of generators but have only ansi c realization so it is not very fast
Intel MKL uses only SSE extension and no support for paralleling
And so on
From the table we can conclude that
Now there is no generators that uses avx512
The purpose of my work is to accelerate rngavxlib.

## Slide 8: RNGAVXLIB (AVX2)
МИЭМ НИУ ВШЭ, 2018
Генераторы | GM19, GM29, GM31, GM55, GM61, GQ58.1, GQ58.3, GQ58.4, LFSR113, MRG32K3A, MT19937
Интерфейс | void rng_init_(rng_state* state); void rng_skipahead_(rng_state* state, unsigned long long offset); unsigned int rng_ansi_generate_(rng_state* state); unsigned int rng_sse_generate_(rng_state* state); unsigned int rng_avx_generate_(rng_state* state);
SIMD | ANSI C, SSE2, SSE4.1, AVX2
Языки | C, Fortran
Генератор | Скорость (Gbit/sec)
GM19 | 
GM29 | 
GM31 | 
GM55 | 
GM61 | 
GQ58.1 | 
GQ58.3 | 
GQ58.4 | 
LFSR113 | 
MRG32K3A | 
MT19937 | 
Intel Core i7-4790K (4 GHz);
Compiler: gcc; Optimization level: -O3
Notes: Rngavxlib consists of 11 modern and reliable generators. It has ansi c, sse, and avx2 versions of each generator. They produce the same sequences, but obviously avx2 version is the fastest.

## Slide 9: Результаты 1
МИЭМ НИУ ВШЭ, 2018
 | ANSI C | SSE | AVX2 | AVX512
GM19 | 0,02 | 0,30 | 0,46 | 0,82
GM29 | 0,02 | 0,36 | 0,50 | 0,90
GM31 | 0,01 | 0,22 | 0,38 | 0,67
GM55 | 0,08 | 0,48 | 0,53 | 0,72
GM61 | 0,01 | 0,12 | 0,18 | 0,33
GQ58X1 | 0,02 | 0,14 | 0,21 | 0,36
GQ58X3 | 0,05 | 0,31 | 0,33 | 0,37
GQ58X4 | 0,09 | 0,42 | 0,46 | 0,66
MRG32K3A | 0,18 | 0,83 | 0,92 | 1,07
MT19937 | 0,30 | 1,36 | 1,45 | 1,47
LFSR113 | 0,42 | 1,15 | 2,48 | 4,04
PHILOX4X32X10 | 0,24 | 0,59 | 0,81 | 0,98
Intel(R) Xeon Phi(TM) CPU 7210 @ 1.30GHz
Compiler: gcc; Optimization level: –O0
Notes: In avx512 version philox of library has been added.
On this slide you can see the results for gcc compiler on optimization level –O0
In the table speed of each version is written . It is in gbits per second. And the right graph represents this data.
For each generator avx512 gives an acceleration. The biggest one is for lfsr113. this generator state consist only of 4 numbers, so zmm register can contain 4 such states. Avx512 version uses this facts and calculates four numbers at the same time.

## Slide 10: Результаты 2
МИЭМ НИУ ВШЭ, 2018
 | ANSI C | SSE | AVX2 | AVX512
GM19 | 0,02 | 0,29 | 0,43 | 0,70
GM29 | 0,02 | 0,34 | 0,45 | 0,74
GM31 | 0,01 | 0,22 | 0,36 | 0,57
GM55 | 0,06 | 0,43 | 0,44 | 0,65
GM61 | 0,01 | 0,11 | 0,17 | 0,30
GQ58X1 | 0,02 | 0,14 | 0,21 | 0,34
GQ58X3 | 0,03 | 0,30 | 0,30 | 0,33
GQ58X4 | 0,06 | 0,38 | 0,40 | 0,59
MRG32K3A | 0,97 | 1,37 | 1,71 | 2,57
MT19937 | 1,57 | 3,16 | 3,80 | 4,26
LFSR113 | 1,89 | 1,41 | 1,52 | 6,27
PHILOX4X32X10 | 1,35 | 0,97 | 1,51 | 2,33
Intel(R) Xeon Phi(TM) CPU 7210 @ 1.30GHz
Compiler: gcc; Optimization level: –O3
Notes: Here the same calculations but for optimization level –O3
With this optimization speeds are higher than for o0 optimizations.
Somewhere sse version is slower than ansi .

## Slide 11: Заключение
МИЭМ НИУ ВШЭ, 2018
12 генераторов псевдослучайных чисел были реализованы с использованием AVX512
Новые версии генераторов воспроизводят в точности оригинальные последовательности
Среднее и максимальное ускорение для компилятора: gcc; Optimization level –O0
  AVX512 к ANSI C: 20.12, 48.85;
  AVX512 к SSE: 2.12, 3.50;
  AVX512 к AVX2: 1.49, 1.87;
Среднее и максимальное ускорение для компилятора : gcc; Optimization level –O3
  AVX512 to ANSI C: 21.44, 54.49;
  AVX512 to SSE: 2.21, 4.45;
  AVX512 to AX2: 1.72, 4.12.
Notes: All the generators have been implemented with avx512 instructions and zmm registers.
They all works properly, and give the same sequence as previous versions
On average avx 512 is 20 times faster than ansi c version for o0 optimization level
In compare with avx2 version avx512 faster